New Zealand Geodetic Datum 2000 Projections

LINZG25702

This fact sheet describes the NZGD2000 projections that have been defined for representation of spatial data in New Zealand, its offshore islands, and the continental shelf

Further information

LINZ standards, fact sheets and up-to-date information are available on the LINZ website: http://www.linz.govt.nz.

Further information is available from:

Surveyor-General

Land Information New Zealand

PO Box 5501

Lambton Quay

Wellington 6145

Email: info@linz.govt.nz

LINZ has defined a series of map projections in terms of the New Zealand Geodetic Datum 2000 (NZGD2000) for topographic mapping and spatial data representation over New Zealand, its offshore islands, and the continental shelf.

Each of the NZGD2000 projections is defined in LINZS25002 Standard for New Zealand Geodetic Datum 2000 Projections: Version 2.  This standard was originally published in November 2007 and was amended in July 2008.  NZGD2000 is defined in a separate standard, LINZS25000 Standard for New Zealand Geodetic Datum 2000.

NZGD2000 projections have been defined to support topographic mapping of the New Zealand mainland, its offshore islands, and the continental shelf.  In addition, there are meridional circuits for cadastral surveying on the New Zealand mainland and the coastal islands.  Each projection is described in the following sections.

Transformation of coordinates between NZGD2000 projections and projections in terms of other datums, such as NZGD1949, is explained in the fact sheet LINZG25703 Datum and Projection Transformations.

New Zealand Transverse Mercator 2000 projection

The New Zealand Transverse Mercator 2000 (NZTM2000) is the official projection for LINZ medium scale topographic mapping on the New Zealand mainland and its coastal islands.  NZTM2000 is being used for the new 1:50,000 map series, Topo50 (available from September 2009).

This projection supersedes the NZGD1949 based New Zealand Map Grid (NZMG) that has been used for the NZMS260 1:50,000 mapping.  NZTM2000 has greater international consistency and is more easily incorporated into mapping applications and equipment.

Assistance for the conversion of coordinates between NZMG and NZTM2000 is available on the LINZ website.

The key parameters of NZTM2000 are:

Projection name	New Zealand Transverse Mercator 2000

Abbreviation	NZTM2000

Datum		NZGD2000

Reference ellipsoid	GRS80

Origin latitude	0° 00’ South

Origin longitude	173° 00’ East

False northing	10,000,000 metres North

False easting	1,600,000 metres East

Central meridian scale factor	0.9996

| Meridional circuits New Zealand cadastral survey data is typically presented in terms of a local projection. Surveys that are carried out on the New Zealand mainland and its coastal islands using NZGD2000 are displayed in one of 28 local Transverse Mercator projections called meridional circuits. The parameters defining the meridional circuits are available in LINZS25002 and on the LINZ website. Offshore island projections New Zealand has jurisdiction over a number of offshore islands. To enable the presentation of spatial data, topographic mapping and cadastral surveys on New Zealand’s offshore islands, five additional Transverse Mercator projections have been defined in terms of NZGD2000. Geospatial data cannot be represented using NZTM2000 in offshore areas due to the large distortion that occurs on Transverse Mercator projections with increasing distance from the central meridian. The common parameters for the offshore island projections are: Datum NZGD2000 Reference ellipsoid GRS80 Origin latitude 0° 00’ South False northing 10,000,000 metres North False easting 3,500,000 metres East Central meridian scale factor 1.0000 The remaining parameters for the offshore island projections are listed in the table below: |  | New Zealand Continental Shelf 2000 projection The New Zealand Continental Shelf Lambert Conformal 2000 (NZCS2000) projection is suitable for the presentation of datasets that span the New Zealand continental shelf. The continental shelf extends from 25°S to 60°S and from 160°E to 170°W. Unlike the other projections on this fact sheet, NZCS2000 is a Lambert Conformal Conic projection. This is to minimise the distortion that occurs with transverse Mercator projections with increasing distance from the central meridian. The key parameters of NZCS2000 are: Projection name New Zealand Continental Shelf Lambert Conformal 2000 Abbreviation NZCS2000 Datum NZGD2000 Reference ellipsoid GRS80 First standard parallel 37° 30’ South Second standard parallel 44° 30’ South Origin latitude 41° 00’ South Origin longitude 173° 00’ East False Northing 7,000,000 metres North False Easting 3,000,000 metres East Geodetic Reference System 1980 (GRS80) Parameter Value Semi-major axis 6,378,137 metres Inverse flattening 298.257 222 101 |
| --- | --- | --- |

Offshore Island Projection Parameters

| Area | Projection name | Abbreviation | Origin Longitude |
| --- | --- | --- | --- |
| Chatham Islands | Chatham Islands Transverse Mercator 2000 | CITM2000 | 176° 30’ West |
| Snares and Auckland Islands | Auckland Islands Transverse Mercator 2000 | AKTM2000 | 166° 00’ East |
| Campbell Island | Campbell Island Transverse Mercator 2000 | CATM2000 | 169° 00’ East |
| Antipodes and Bounty Islands | Antipodes Islands Transverse Mercator 2000 | AITM2000 | 179° 00’ East |
| Raoul Island and Kermadec Islands | Raoul Island Transverse Mercator 2000 | RITM2000 | 178° 00’ West |