Standard for New Zealand Vertical Datum 2009

LINZS25004

Effective date 14 September 2009

Table of Contents

TERMS AND DEFINITIONS	3

FOREWORD	5

Introduction	5

Purpose of standard	5

Brief history of standard	5

Committee responsible for standard	5

References	6

1	Scope	7

2	Intended use of standard	7

3	New Zealand Vertical Datum 2009	8

3.1	Official reference surface	8

3.2	Official height system	8

3.3	Normal–orthometric correction	9

4	Local Vertical Datums	10

5	Height Transformations	11

5.1	Introduction	11

5.2	Transformation between NZGD2000 and NZVD2009	11

5.3	Transformation between a local vertical datum and NZVD2009	11

5.4	Transformation between local vertical datums	12

5.5	Transformation between a local vertical datum and NZGD2000	12

Tables

Table 1:  GRS80 gravity field parameters (Moritz 2000)	9

Table 2:  Official local vertical datums and offsets from NZVD2009 	10

Table 3:  New Zealand Local Vertical Datums	15

TERMS AND DEFINITIONS

For the purposes of this standard, the following terms and definitions apply.

| Term/abbreviation | Definition |
| --- | --- |
| ellipsoid | a surface formed by the rotation of an ellipse about a main axis. For the purposes of this standard, the ellipsoids used are oblate to match the general shape of the Earth. An oblate ellipsoid is one in which the semi–minor axis of the ellipse is the axis of revolution. |
| ellipsoidal height | the distance from a reference ellipsoid to a point along the ellipsoidal normal |
| equipotential surface | a surface that is always perpendicular to the force of gravity. An example is the surface of the ocean, if disturbances caused by influences such as tides, currents, seawater density, wind, and atmospheric pressure are not considered. |
| geoid | an equipotential surface that is approximated by sea level in the open oceans and which is the reference surface for orthometric heights |
| GRS67 | Geodetic Reference System 1967 — a set of parameters adopted by the International Union of Geodesy and Geophysics in 1967 that includes a reference ellipsoid and a normal gravity field for the Earth (IAG 1967) |
| GRS80 | Geodetic Reference System 1980 — a set of parameters adopted by the International Association of Geodesy that includes a reference ellipsoid and a normal gravity field for the Earth (Moritz 2000) |
| LVD | local vertical datum |
| normal height | the distance from the quasigeoid to a point along the curved normal gravity plumbline. Normal heights are calculated along levelling lines using actual gravity observations |
| normal–orthometric height | the distance from the quasigeoid to a point along the curved normal gravity plumbline. Normal–orthometric heights are calculated along levelling lines using a normal gravity field rather than actual gravity observations. |
| NZGD2000 | New Zealand Geodetic Datum 2000, a three-dimensional geocentric datum based on the International Terrestrial Reference Frame 1996 with ellipsoidal heights defined in terms of the GRS80 ellipsoid |
| NZGeoid2009 | New Zealand Quasigeoid 2009 |
| NZGeoid2009 grid | the grid file of NZGeoid2009 values as provided on the LINZ website |
| NZVD2009 | New Zealand Vertical Datum 2009 |
| orthometric height | the distance from the geoid to a point along the plumbline. Orthometric heights can not be easily realised in practice because their calculation requires knowledge of density variations inside the local topography, as well as local gravity. |
| quasigeoid | a non–equipotential surface that coincides reasonably closely with the geoid and which is the reference surface used for normal and normal-orthometric heights |
| quasigeoid height | the vertical distance from the reference ellipsoid to the quasigeoid |
| vertical datum | a curved or level reference surface from which to determine elevations |

FOREWORD

Introduction

A national geodetic system is a fundamental component of a nation’s infrastructure.  The unique property of a geodetic system is its ability to allow the integration of multiple geographically dependent data sources into a single geographic reference frame.

One element of a geodetic system is a national vertical datum.  Transformations are needed to enable spatial data held in terms of other vertical datums to be converted to the national vertical datum.  This allows diverse spatial datasets to be correctly correlated and compared within a consistent framework.

A key benefit of the New Zealand Vertical Datum 2009 (NZVD2009) is the ability to readily determine heights in terms of it anywhere within New Zealand’s territory without resorting to the cost and limitations of precise levelling.

Purpose of standard

The purpose of this standard is to specify a national vertical datum for New Zealand and to define its relationship to other commonly used height systems.

Brief history of standard

This is a new standard.

Committee responsible for standard

The expert committee responsible for reviewing this standard consisted of the following representatives.

| Business Group/Company | Name |
| --- | --- |
| GNS Science | John Beavan |
| LINZ, Business & Regulatory Assurance | Apanui Williams |
| LINZ, Customer Services | Nic Donnelly |
| LINZ, Office of the Surveyor-General | Don Grant Matt Amos |
| LINZ, Regulatory Frameworks & Processes | Mel Amuimuia Michelle Gooding Ruth Willis |
| Local Government New Zealand | Michael Brownie |
| NIWA | Rob Bell |
| University of Otago, School of Surveying | Robert Tenzer |

References

Claessens S, Hirt C, Featherstone W, Kirby J 2009 Computation of a new gravimetric quasigeoid model for New Zealand, technical report prepared for Land Information New Zealand by Western Australia Centre for Geodesy, Curtin University of Technology, Perth, p. 39.

Department of Survey and Land Information 1989, Geodetic Survey Branch Manual of Instruction, DoSLI, Wellington, p. 117.

Heck, B. 2003, Rechenverfahren und Auswertemodelle der Landesvermessung, 3rd edn, Wichman, Karlsruhe, p. 473.

International Association of Geodesy 1967, Geodetic Reference System 1967, Special Publication 3, International Association of Geodesy, Paris, p. 116.

Moritz, H. 2000, Geodetic Reference System 1980, Journal of Geodesy, vol. 74, no. 1, pp. 128-133.

# Scope

- This standard describes the national vertical datum, New Zealand Vertical Datum 2009 (NZVD2009).

- This standard enables the transformation of NZVD2009 heights to and from the 13 major precise levelling–based local vertical datums (LVDs) and the New Zealand Geodetic Datum 2000 (NZGD2000).

# Intended use of standard

Any person using or referring to NZVD2009 must comply with this standard.

COMMENTARY Spatial extent of NZVD2009 NZVD2009 should only be used within the area defined by 160°E to 170°W and 25°S to 60°S.

# New Zealand Vertical Datum 2009

## Official reference surface

- NZVD2009 heights must be measured in relation to the official reference surface.

- The official reference surface of NZVD2009 is the New Zealand Quasigeoid 2009 (NZGeoid2009).

## Official height system

- NZVD2009 heights must be provided in the normal–orthometric height system in relation to the official reference surface.

- The value of the NZGeoid2009 in relation to the Geodetic Reference System 1980 (GRS80) ellipsoid at a specific location must be bi–linearly interpolated from the NZGeoid2009 grid using its NZGD2000 position.

## Normal–orthometric correction

- NZVD2009 normal–orthometric heights must be calculated using the GRS80 normal gravity field specified in Table 1.

- NZVD2009 normal–orthometric heights determined by precise levelling must be reduced using the normal–orthometric correction (NOC) equation (Heck 2003) and GRS80 parameters specified in Table 1:

expressed in metres

where

|  | is the GRS80 normal gravity flattening constant |
| --- | --- |
|  | GRS80 mean Earth radius, expressed in metres |
|  | average normal-orthometric height of benchmarks, expressed in metres |
|  | mid–latitude between benchmarks |
|  | azimuth between benchmarks |
|  | horizontal distance between benchmarks, expressed in metres. |

Table 1:  GRS80 gravity field parameters (Moritz 2000)

| Parameter | Symbol | Value |
| --- | --- | --- |
| normal gravity flattening constant |  | 0.005 302 440 112 |
| mean Earth radius |  | 6 371 000 m |

- Where NZVD2009 normal-orthometric heights are determined by precise levelling the NOC must be calculated in relation to a mark with an existing NZVD2009 height that is included in the levelling line.

COMMENTARY Historic normal–orthometric correction The normal–orthometric correction used for precise levelling reductions in New Zealand before this standard became effective is defined in Appendix B.

# Local Vertical Datums

- The official LVDs defined in Table 2 may be used with NZVD2009.

- The offsets defined in Table 2 must be used to relate NZVD2009 to the official LVDs.

Table 2:  Official local vertical datums and offsets from NZVD2009,

| Local vertical datum | Offset to NZVD2009 (m) |
| --- | --- |
| One Tree Point 1964 | 0.06 |
| Auckland 1946 | 0.34 |
| Moturiki 1953 | 0.24 |
| Gisborne 1926 | 0.34 |
| Napier 1962 | 0.20 |
| Taranaki 1970 | 0.32 |
| Wellington 1953 | 0.44 |
| Nelson 1955 | 0.29 |
| Lyttelton 1937 | 0.47 |
| Dunedin 1958 | 0.49 |
| Dunedin-Bluff 1960 | 0.38 |
| Bluff 1955 | 0.36 |
| Stewart Island 1977 | 0.39 |

# Height Transformations

## Introduction

The following paragraphs define the transformations between official New Zealand height systems.  The transformations defined are between:

- NZGD2000 and NZVD2009,

- LVDs and NZVD2009,

- different LVDs, and

- LVDs and NZGD2000.

## Transformation between NZGD2000 and NZVD2009

When transforming between NZGD2000 ellipsoidal heights and NZVD2009 normal-orthometric heights, the following equations must be used:

where

|  | is the NZVD2009 normal–orthometric height in metres |
| --- | --- |
|  | is the NZGD2000 ellipsoidal height in metres |
|  | is the NZGeoid2009 value in metres at the NZGD2000 position of . |

## Transformation between a local vertical datum and NZVD2009

When transforming between normal–orthometric heights in terms of a LVD listed in Table 2 and NZVD2009 normal–orthometric heights, the following equations must be used:

where

|  | is the NZVD2009 normal–orthometric height in metres |
| --- | --- |
|  | is the LVD normal–orthometric height in metres |
|  | is the LVD offset from Table 2. |

## Transformation between local vertical datums

When transforming normal–orthometric heights between the LVDs listed in Table 2, the following equation must be used:

where

|  | is the LVD normal–orthometric height in metres |
| --- | --- |
|  | is the LVD normal–orthometric height in metres |
|  | is the LVD offset from Table 2 |
|  | is the LVD offset from Table 2. |

## Transformation between a local vertical datum and NZGD2000

When transforming between normal–orthometric heights in terms of a LVD listed in Table 2 and NZGD2000 ellipsoidal heights, the following equations must be used:

where

|  | is the NZGD2000 ellipsoidal height in metres |
| --- | --- |
|  | is the LVD normal–orthometric height in metres |
|  | is the NZGeoid2009 value in metres at the NZGD2000 position of |
|  | is the LVD offset from Table 2. |

Appendix A:  Height systems

Introduction

A height is a vertical distance above a reference surface.  The type of reference surface used has an impact on the type of height that can be measured from it.  Normal-orthometric and ellipsoidal are the two types of height that are commonly used in New Zealand.

Normal–orthometric heights

- Normal–orthometric heights correspond to what most users understand as heights above mean sea level.

- Normal-orthometric heights are approximations of true orthometric heights within the limits of approximation of the normal gravity field to the actual gravity field.

- The flow of fluids is more realistically predicted by normal-orthometric heights than by ellipsoidal heights.

Ellipsoidal heights

- Ellipsoidal heights are measured above a reference ellipsoid.

- The GRS80 ellipsoid is a simple geometric approximation of the shape of the geoid that varies from mean sea level by up to about ±100 m globally.

- Ellipsoidal heights cannot reliably predict the flow of fluids because the ellipsoid does not relate to the Earth’s gravity field.

- Ellipsoidal heights are provided in Global Navigation Satellite System positions because of their geometrically simple definition.

- NZGD2000 uses ellipsoidal heights based on the GRS80 ellipsoid.

Appendix B:  Historic normal–orthometric correction

Before this standard became effective, normal–orthometric heights that were established by precise levelling were reduced using the following Geodetic Reference System 1967 normal–orthometric correction (NOCGRS67) equation (The Department of Survey & Land Information 1989):

expressed in metres

where

|  | equals 0.002 506 |
| --- | --- |
|  | equals 0.000 007 |
|  | is the mid–latitude between benchmarks |
|  | is one minute of arc in radians (~0.0002908882) |
|  | is the average height of benchmarks, expressed in metres |
|  | is the difference in latitude between benchmarks, expressed in arc–minutes, positive southwards. |

Appendix C:  Background information for local vertical datums

This appendix contains useful background information about the local vertical datums for which offsets to NZVD2009 are provided in Table 2.

Table 3:  New Zealand Local Vertical Datums

| Local vertical datum | Code | Data used to define datum | Reference mark name | Reference mark geodetic code | Reference mark height in terms of LVD (m) | Offset to NZVD2009 (m) | Standard deviation (m) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| One Tree Point 1964 | ONTPHT1964 | 1960 – 1963 | RNZN BM | DJM9 | 3.139 | 0.06 | 0.03 |
| Auckland 1946 | AUCKHT1946 | 1909 – 1923 | 98-21 SO 69501 | DD1N | 3.491 | 0.34 | 0.05 |
| Moturiki 1953 | MOTUHT1953 | 1949 – 1952 | BC 84 | B309 | 3.141 | 0.24 | 0.06 |
| Gisborne 1926 | GISBHT1926 | 1926 | GB 01 | ACVP | 3.039 | 0.34 | 0.02 |
| Napier 1962 | NAPIHT1962 | Unknown | H 40 | B3XM | 3.913 | 0.20 | 0.05 |
| Taranaki 1970 | TARAHT1970 | 1918 – 1921 | New Plymouth Fundamental | AGMH | 4.906 | 0.32 | 0.05 |
| Wellington 1953 | WELLHT1953 | 1909 – 1946 | K 80/1 | ABPB | 2.087 | 0.44 | 0.04 |
| Nelson 1955 | NELSHT1955 | 1939 – 1942 | N 1 | AC4T | 3.532 | 0.29 | 0.07 |
| Lyttelton 1937 | LYTTHT1937 | 1918 – 1933 | UD 40 | B40V | 3.165 | 0.47 | 0.09 |
| Dunedin 1958 | DUNEHT1958 | 1918 – 1937 | WW 83 | AFEQ | 2.737 | 0.49 | 0.07 |
| Dunedin-Bluff 1960 | DUBLHT1960 | No sea level data used | Z 41 | B3R8 | 112.699 | 0.38 | 0.04 |
| Bluff 1955 | BLUFHT1955 | 1918 – 1934 | Bluff Fundamental | ABCC | 7.011 | 0.36 | 0.05 |
| Stewart Island 1977 | STISHT1977 | 1976 – 1977 (5 tides only) | N (Paterson SD) | A017 | 44.10 | 0.39 | 0.15 |

# Footnotes

For more information about height systems, see Appendix A: Height systems.

For more information about the local vertical datums, see Appendix C.

A description of how the offsets were computed is provided in Claessens et al. (2009)