If you have any comments?

Please provide supporting reasons for your comments and suggested wording for proposed changes.

| Email: | imagery@linz.govt.nz |
| --- | --- |

| Postal address | Physical address |
| --- | --- |
| Land Information New Zealand | Land Information New Zealand |
| PO Box 5501 | Level 7, Radio New Zealand House |
| WELLINGTON 6145 | 155 The Terrace |
|  | WELLINGTON |

Table of contents

Terms and definitions	3

General	3

Term/abbreviation	3

Definition	3

Purpose	3

How to use this Guideline	3

Background	3

Introduction	3

Scope	3

Intended users of specifications	3

References	3

Brief history of specifications	3

Attribution	3

1   Specifications for the procurement of orthophotography	3

1.1	Coverage	3

Coverage	3

1.2	Resolution and accuracy	3

Radiometric & spectral resolution – requirements	3

Ground sample distance (GSD)	3

Horizontal accuracy	3

Spatial control – responsibility	3

1.3	Imagery acquistion requirement	3

Sensor requirements	3

Sun angle	3

Atmospheric effects	3

Cloud cover	3

Coastal photography	3

1.4	Orthorectification	3

Datum and projection	3

Undertaking orthorectification	3

Tiling requirements	3

1.5	Deliverables	3

Delivery	3

Image formats	3

Products delivery	3

Vector GIS products	3

Optional products	3

Metadata	3

1.6	Copyright	3

Copyright	3

1.7	Tender Response	3

The Tender response	3

1.8	Metadata	3

Metadata statements	3

Metadata format	3

Project metadata	3

Dataset metadata	3

1.9	Data Delivery	3

Data Delivery	3

1.10	Detailed Metadata Requirements	3

Project Metadata Requirements	3

Dataset Metadata Requirements	3

2  Specifications for quality assurance of orthophotography	3

2.1	Quality assessment	3

Quality process	3

Quality plan	3

Sample images	3

Review of ortho-photography	3

2.2	Aesthetic quality guidelines	3

Criteria	3

Radiometry	3

Brightness	3

Shadows	3

Contrast	3

Colour balance	3

Foreign artefacts	3

Elevated features	3

## Terms and definitions

| General | For the purposes of this specification, the following terms and definitions apply. |
| --- | --- |

| Term/abbreviation | Definition |
| --- | --- |
| FCC | False colour composite. Features that are red appear green, green features (except vegetation) appear blue, and “infrared” features, which normally are not seen at all, appear red. The primary use FCC imagery is vegetation study and identification. This is because healthy green vegetation is a very strong reflector of infrared radiation and appears bright red. |
| Orthorectification | An orthophoto is an aerial photograph geometrically corrected (“orthorectified”) to ensure the scale is uniform: the photo has the same lack of distortion as a map. Unlike an uncorrected aerial photograph, an orthophotograph can be used to measure true distances, because it is an accurate representation of the Earth’s surface, having been adjusted for topographic relief, lens distortion, and camera tilt. The image has been corrected to ensure that horizontal scale is constant. |
| Radiometric resolution | Radiometric resolution determines how finely a system can represent or distinguish variations of intensity. Higher values mean that more subtle appearance changes in an image can be detected. Radiometric resolution can be measured in bits, for example 8 bits. |
| Raw images | For the purpose of this document Raw images refer to images that have not been orthorectified or tiled. |
| RGB | Natural Colour (red, blue, green), images offer a natural colour rendition. This means the colour of an object in the image is the same colour as if you viewed the object in person e.g. a green tree appears green. |
| RGBI | Four Band (red, blue, green, near infra-red) images are similar to natural colour, however, trees, crops and things with chlorophyll appear red in colour. |
| NZ Public Sector | This includes territorial authorities, regional councils, and central government agencies in New Zealand |
| Contractor | For the purpose of this document Contractor refers to the supplier of the orthophotography. |
| GSD | Ground sample distance (also referred to as Pixel size) for an orthophoto is the distance on the ground, measured in x and y components, represented by each pixel in the image. |
| Spectral resolution | Spectral resolution refers to the number of different frequency bands recorded. |

Foreword

| Purpose | The purpose of this document is to provide a common specification to assist the New Zealand public sector with the procurement of ‘standard’ orthophotography, in support of the National Imagery Coordination effort. Orthophotograhy provides a key location-based reference for policy and decision-makers at all levels, and has many applications within business and the day-to-day life of our citizens. |
| --- | --- |

| How to use this Guideline | PART 1 and 2 will form the product requirement part of your tender. Simply delete the commentary boxes from each section that are supplied to aid your decision making process. |
| --- | --- |

| Background | Geospatial information (location-based information) is increasingly recognised as an enabler of quality policy and decision making. It underpins well-informed decisions, drives efficiencies in public services, and facilitates growth in the private sector. To release the full potential of geospatial information the data needs to be collected and maintained to consistent standards, be readily discoverable, accessible, and interoperable. Improving the coordination of imagery acquisition, access and dissemination will enable this information to be widely re-used and generate benefits to the wider New Zealand economy. The New Zealand Geospatial Office identified imagery as one of 13 fundamental geospatial data themes, a key asset of the Crown, and critical to the effective running of New Zealand. Imagery is used by many public and private organisations and has become essential for many business functions, as it informs and improves the quality of decisions. Imagery is used in a wide range of applications including emergency response, hazard management, civil planning, defence, topographic mapping, land use analysis, hydrology, property boundary analysis, asset management, demographic studies, logistics / transportation, change detection, environmental monitoring, emissions trading, precision agriculture, agricultural forecasting, monitoring water quality and more. |
| --- | --- |

| Introduction | This Document consists of two parts. Part 1 - Procuring orthophotography Procuring orthophotography is not a simple process. Technical knowledge within agencies procuring orthophotography is often low due to the irregular frequency of commissioning the services, leading to incorrect, excessive, or irrelevant products being obtained. This situation also affects the suppliers of orthophotography by increasing the cost and effort required to tender for work. Efficiencies can be made through the use of common specifications when procuring orthophotography. Procuring agencies can be confident that the necessary requirements for 'standard' acquisitions are properly defined, and contractors can efficiently tender for work due to the requirements being consistently and clearly stated. Part 2 - Quality of orthophotography Most problems with orthophotography can be grouped into two categories: quantifiable and subjective. Quantifiable problems, such as improperly geo-referenced or distorted imagery, should be fixed by contractors. Subjective problems generally are aesthetic, but they are important in ensuring the true value and usefulness of orthophotography. The quantifiable components of orthophotography quality will be defined in the contract document or its technical specification. |
| --- | --- |

| Scope | This document provides: a common set of specifications and guidance notes for the purchase of orthophotography by the public sector in New Zealand. The requirements can also be used by non-government organisations, a common definition of quality acceptance measures and a method for obtaining agreement between orthophotography purchasers and contractors. |
| --- | --- |

| Intended users of specifications | These specifications are intended to be used by any organisation within New Zealand when: purchasing new orthophotography, and assessing the quality of this orthophotography prior to acceptance from the contractor. |
| --- | --- |

| References | The following documents are necessary for the application of these specifications: Australia and New Zealand Land Information Council (ANZLIC) Metadata Profile (version 1.1) ANZMet Lite Collection Tool (version 1.2) Cox, S (1999) Now that’s a good-looking Orthophoto!, Geo World, 12(11):50-53 |
| --- | --- |

| Brief history of specifications | In these specifications: PART 1: Specifications for orthophotography are new, and PART 2: Specifications for aesthetic quality of orthophotography have been derived from an article by Scott Cox . |
| --- | --- |

| Attribution | This copyright work is licensed under the Creative Commons Attribution 3.0 New Zealand licence. To view a copy of this licence, visit http://creativecommons.org/licenses/by/3.0/nz/. |
| --- | --- |

# Specifications for the procurement of orthophotography

## Coverage

| Coverage | Coverage – The product required in this schedule will be provided over the entire area shown in the figure below The product required in this schedule will include a two kilometre sea buffer, but excluding the rest of the sea. <<Insert a map of the coverage area that you are requiring imagery for>> |
| --- | --- |

## Resolution and accuracy

| Radiometric & spectral resolution – requirements | Type Radiometric resolution Spectral resolution Natural colour (RGB) 24-bit colour (3 x 8 bits per band) Red, blue, green Four band (RGBI) 32-bit colour (4 x 8 bits per band) Red, blue, green, near infra-red False colour composite (FCC) 24-bit colour (3 x 8 bits per band) Near infra-red (displayed in red), blue, green Delete the above radiometric and spectral resolution products that you do not require. COMMENTARY When selecting the orthophotography type, purchasers need to ensure that the radiometric and spectral resolution conforms to one, or more, of the specifications set out in the table above |
| --- | --- |

| Ground sample distance (GSD) | The ground sample distance (GSD) for the outlined coverage area is to be <<enter your value here>> metres. COMMENTARY GSD – Ground sample distance (also referred to as Pixel size) for an orthophoto is the distance on the ground, measured in x and y components, represented by each pixel in the image. For example, in an orthophoto with a 1 metre GSD, each pixel is the equivalent of 1 metre by 1 metre on the ground. Your organisations planned uses of orthophotography will help dictate the resolution you require. The table below is a guide typically uses for resolutions GSD Commons uses 0.125 metre or better City, Urban and developed area mapping and feature identification examples of features include manholes covers, fire hydrants, curbs and gutters. 0.5 metre or better Rural and less developed area mapping and feature identification examples of features include buildings and roads. 10 metre or better National land cover usage. Selecting the correct GSD is important to ensure you can identify the features required. It is also important not to specify a GSD that costs more without any practical benefit in doing so. If your organisation is unsure what types of features can be captured from each output GSD, you should contact one of the aerial imagery companies to discuss. |
| --- | --- |

| Horizontal accuracy | The horizontal accuracy of the orthophotography is to be <= +/- <<enter your value here>> metres. 90% confidence interval COMMENTARY Horizontal accuracy of the orthophotography needs to be specified for all new orthophotograpy. Horizontal Accuracy should be specific in metres E.g. <= +/- 3.0 metres. 90% confidence interval The table below is a guide of accuracy typically required GSD Horizontal accuracy (metres) 0.1 metres <= +/- 0.3 metres 0.2 metres <= +/- 1.0 metres 0.4 metres <= +/- 3.0 metres Horizontal accuracy Horizontal accuracy (also referred to as Spatial or Positional Accuracy) is a measure of the distance of an image from its true position. Accuracy Considerations Typically, greater horizontal accuracy is required in City and Urban areas than in rural areas. Where an organisation has urban and rural requirements horizontal accuracy will need to suit the GSD of the each imagery set. Ensure that accuracy is at the highest level required within your organisation or consortium e.g. planning uses typically require less accuracy than engineering uses. Improving horizontal accuracy can be achieved in three ways Better positioning of the image centre – more accurately determining the true location of the camera as the image is captured. Increased amount of ground control. Be aware that this will usually be accompanied by an increase in cost. Increase the density & quality of the Digital Terrain Model (DTM). Be aware that this will usually be accompanied by an increase in cost. |
| --- | --- |

| Spatial control – responsibility | The contractor is responsible for providing any ground control necessary to meet the spatial accuracy specified above. |
| --- | --- |

## Imagery acquistion requirement

| Sensor requirements | All imagery must be captured using a fully calibrated large format airborne digital camera system. COMMENTARY A number of documents may need to be sighted to support the contractor compliance with this requirement. See Section 1.7 - Tender response |
| --- | --- |

| Sun angle | The sun angle at the time of the imagery capture must be more than 35° above the horizon. Imagery captured over urban and commercial areas must be undertaken at a time of the day that will minimise the shadows cast by tall buildings etc, capture must be more than 40° above the horizon. COMMENTARY The value can be negotiated e.g. for late season flying, areas of flat rolling terrain, and in areas where large water bodies are present, but the value must be stated in the contract. |
| --- | --- |

| Atmospheric effects | Image detail and clarity must not be lost as a result of atmospheric conditions including haze, smoke, dust, and environmental factors. |
| --- | --- |

| Cloud cover | All Orthophotos must be 100% cloud free. |
| --- | --- |

| Coastal photography | Estuarine, shallow coastal environments, and reefs will be acquired within two hours of low tide. These areas will be identified in the coverage diagram. COMMENTARY The value can be negotiated but must be agreed in writing in advance of the imagery being acquired. |
| --- | --- |

## Orthorectification

| Datum and projection | All orthophotography will be provided in the New Zealand Transverse Mercator 2000 projection (NZTM2000). The datum is New Zealand Geodetic Datum 2000 (NZGD2000). |
| --- | --- |

| Undertaking orthorectification | The Orthorectification process must be undertaken in a manner that ensures: straight lines on the ground are straight in the image, common overall scale and resolution is maintained, building lean is minimised, differences in contrast and brightness between images within a tile are minimised, the joins between all tiles are seamless, with no gaps, overlaps, or visible join lines between adjacent images, the pixels on adjacent tiles must align, features at ground level are continuous across mosaic seam lines eg valleys, ridges, buildings, and roads etc, no duplication of features occurs along seam lines, and cloned features used to ‘touch up’ features that are obscured in images must be used with caution and kept to a minimum. |
| --- | --- |

| Tiling requirements | Orthophotography will be tiled to align with the LINZ Topo50 map sheet breakdown as follows; Nominal scale Tile coverage 1:10,000 4,800 x 7,200 metres 1:5,000 2,400 x 3,600 metres 1:2,000 960 x 1,440 metres 1:1,000 480 x 720 metres 1:500 240 x 360 metres Each tile will be supplied complete; i.e. no partial tiles. (A ‘complete tile’ meaning full tile dimensions, but may not be a full tile of imagery) |
| --- | --- |

## Deliverables

| Delivery | The contractor is responsible for the delivery of all orthophotography to the purchaser, including the cost of all media and courier charges. All data is to be delivered to the purchaser on appropriate portable storage media. Each supplied portable media device must be labeled with the following: Supplier Customer Geographic coverage Date captured. |
| --- | --- |

| Image formats | The format of uncompressed images will be: GeoTIFF, or TIFF with an appropriate geo-referencing file eg TFW, TAB., The format of compressed images will be JPEG2000 , with a maximum compression of 10 times. COMMENTARY The formats above are the most commonly used to deliver orthophotography. If the customer requires the products in any other recognized format this should be specified in this section. |
| --- | --- |

| Products delivery | The contractor shall deliver the following orthophotography products: a single compressed mosaic for the entire acquisition area, and (consider file size, large areas may require a number of files) Individual mosaic tiles based on the Topo50 sheet breakdown.. Mosaic tiles files will be named in the following format: Standard Format of [sheet] [scale] [tile].[ext] Where: Sheet: [Topo50 sheet number] eg BK34 Scale: [nominal scale of mosaic] eg 500 Tile: [Row number. Column number of tile ] eg 074042 Ext: [file extension] eg TIF, TFW, DAT, JP2 (Example will be BK34_500_074042.tif) Optional fields of [type] [year] Type: [type of image] eg RGB, RGBI, FCC Year: [year of acquisition] eg 2012 COMMENTARY The minimum requirement for file names should be the standard format above. If additional fields are required, state this in the tender. The tile numbers and coverage are based on the breakdown of a standard LINZ Topo50 map sheet as in following example. Scale Sheet Number Coverage (m) Tile Number Range (Row,Column) 1:50,000 BQ31 24000 x 36000 The prime rectangle 1:10,000 BQ31-10000/4.5 4800 x 7200 1.1 – 5.5 1:5,000 BQ31-5000/9.7 2400 x 3600 1.1 – 10.10 1:1,000 BQ31-1000/37.21 480 x 720 1.1 – 50.50 1:500 BQ31–500/74.42 240 x 360 1.1 – 100.100 |
| --- | --- |

| Vector GIS products | The contractor will deliver an index of the footprints of the orthophotography tiles supplied in both MapInfo tab file or Esri shape file formats: |
| --- | --- |

| Optional products | The contractor is to deliver the following products. (Delete any that are not required.) The digital terrain model, including break lines if captured, used for orthorectification. A digital index of the raw aerial photography centres and footprints of photography frames (containing date and time of acquisition) Flight lines of aerial photography. Any new ground controls points surveyed for the project. The original overlapping stereo photography Delete the above section or products if they are not required COMMENTARY The contractor will be able to deliver the following products if required and specified in the contract. NOTE; This may incur additional costs. |
| --- | --- |

| Metadata | Metadata will be provided in accordance with section 1.8 of this document for every dataset and each tile delivered to the purchaser, including interim, partial, and final deliverables. |
| --- | --- |

## Copyright

| Copyright | All data and products procured under this guideline will be provided with a licence that enables the purchaser to release the data to any person, group, or organisation under a Creative Commons Attribution 3.0 New Zealand licence (CC by) with attribution to the purchaser in line with the New Zealand Government Open Access Licensing framework (NZGOAL). |
| --- | --- |

## Tender Response

| The Tender response | The following information should be supplied with tender responses: (Delete any that are not required.) Details on how the raw imagery capture is to be undertaken, including methodology, equipment being used, system calibration, sensor parameters , data processing etc; Diagrams of the proposed survey area and flight lines for Imagery including cross strips for each of the options proposed. Diagrams of the proposed survey area and location of planned ground control and check points, and the origin of points (e.g. field measurement for this project or state survey control) for each of the options proposed. Description of the processes to produce the specified data products and how the specified accuracies will be met. Technical qualifications and relevant experience of the company, project team members and project manager in undertaking airborne imagery surveys. This should also include recent examples of similar projects recently completed. Gantt chart or table describing tasks, milestones, deliverables and timeframes in weeks from the day of receipt of purchase order. In addition to the specifications requested, proponents may also wish to offer alternative solutions which could offer cost or time savings to the project. |
| --- | --- |

## Metadata

| Metadata statements | Metadata statements will be provided for: The overall project (Project metadata). Each dataset that is delivered (Dataset metadata). COMMENTARY The project metadata record contains information that pertains to the project as a whole and also to all of the datasets acquired as part of the project. It can be considered to be “parent metadata” A dataset metadata record contains information that relates only to the dataset. It does not contain information about other datasets collected as part of the same project. It can be considered to be “child” metadata. A dataset in the context of this imagery specification can be generally considered as a (usually tiled) collection of orthophotos of the same resolution, usually over a contiguous area, created from images collected under a single contract, in a single flying season, and processed to the same standard. The dataset includes associated files such as georeferencing files. A metadata statement for each file in a dataset is not required. |
| --- | --- |

| Metadata format | Metadata statements will be consistent with the ANZLIC Metadata Profile (version 1.1). Metadata will be provided in XML formatted files. Metadata records must validate against the ANZLIC schematron files. If the metadata files do not validate they will not be accepted. The contract will not be complete until all metadata is satisfactorily supplied. COMMENTARY The ANZLIC metadata profile version 1.1 is a profile of the ISO 19115 (2003) standard. A revision of the ISO standard, ISO 19115-2 (2009) introduced extensions for imagery and gridded data. These specifications for imagery metadata may change when ANZLIC updates its profile. Details of the ANZLIC Metadata Profile can be found at: http://spatial.gov.au/resources/metadata Note that the ANZMet Lite tool referenced in the above webpage will not produce metadata that complies with these specifications. |
| --- | --- |

| Project metadata | Project metadata shall meet minimum ANZLIC metadata requirements. Additional to the minimum requirements, the following information is required: Job No The contractor’s job number Date date of final contract completion Source The source company or agency which acquired the imagery Reference number The source company or agency project reference number Details of the project metadata requirements can be found in section 1.10. |
| --- | --- |

| Dataset metadata | Dataset metadata shall meet core ANZLIC metadata requirements, except as outlined below. Additional to the core requirements, the following information is required: Bands A description of each band of the electromagnetic spectrum that comprise the image. Horizontal accuracies Horizontal tolerances of the photograph's accuracy; usually expressed as '±2.5 pixels'. Sensor information Type of camera acquiring the imagery Medium of photo The material in which the photograph exists, eg. imageDigital Ortho Image Type eg Tiff RGB Image Size X,Y (metres): eg 2,400 x 3,600 Image width, height (pixels) eg 4,800 x 7,200 Pixel size: eg 0.5m Positional accuracy eg ±2.5 pixels Altitude The mean height at which the original images were flown Source The source company or agency which took the photograph The following core elements are not required, as the information is not relevant, not available, or not known to the contractor: Temporal Extent Date range within which the dataset is valid Vertical Extent Maximum and Minimum heights within which the dataset lies. Dataset Responsible Party Party responsible for the dataset. Distribution Format Online distribution format. On-line resource Location from which the resource is available online. Details of the dataset metadata requirements can be found in section 1.10. |
| --- | --- |

## Data Delivery

| Data Delivery | Data deliveries (either electronic or physical) must include a packing slip that, at a minimum, specifies the following: Job title A descriptive title for the contract Job No The contractor’s job number Reference number The source company or agency project reference number Client purchaser name Media type external HDD, DVD, CD Rom No. of media Number of individual media in the delivery Delivery method in person, courier, etc. |
| --- | --- |

## Detailed Metadata Requirements

| Project Metadata Requirements | Description | ANZLIC (Minimum) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
|  |  | Metadata file identifier |  |  | <MD_Metadata.fileIdentifier> |
|  |  | Metadata language |  | eng | <MD_Metadata.language> |
|  |  | Metadata character set |  | Utf8 | <MD_Metadata.characterSet> |
|  |  | Metadata hierarchy level |  | Project | <MD_Metadata.hierarchyLevel> |
|  |  | Metadata hierarchy level name |  | Project | <MD_Metadata.hierarchyLevelName> |
| Client | Client Contact | Metadata contact individual name | Joe Bloggs |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.individualName> |
|  | Client Organisation Name | Metadata contact organisation | Land Information New Zealand |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.organisationName> |
|  | Client Contact Position | Metadata contact position | Imagery Manager |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.positionName> |
|  | Client Role | Metadata contact role |  | Owner | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.role> <CI_RoleCode> |
|  |  | Metadata date stamp |  |  | <MD_Metadata.dateStamp> |
| Job Title | Job Title | Resource title | 2012 Wellington City Council Aerial Imagery Acquisition |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_Citation.title> |

| Project Metadata Requirements | Description | ANZLIC (Minimum) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
| Date | Date of final contract completion | Resource reference date |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_Citation.date> <CI_Date.date> |
|  |  | Resource reference date type |  | Publication | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_Citation.date> <CI_Date.dateType> <CI_DateTypeCode> |
| Project Description | Brief description of the project | Abstract describing the resource | 2012 Rural Colour Photography, Urban Colour Photography, and associated Lidar |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.abstract> |
|  |  | Resource language |  | eng | <MD_Metadata.identificationInfo> <MD_DataIdentification.language> |
|  |  | Resource character set |  | Utf8 | <MD_Metadata.identificationInfo> <MD_DataIdentification.characterSet> |
|  |  | Topic category |  | Imagery base maps earth cover | <MD_Metadata.identificationInfo> <MD_DataIdentification.topicCategory> |

| Project Metadata Requirements | Description | ANZLIC (Minimum) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
| Location | Location Description (e.g. city name, town name, region name, etc) | Geographic location of the resource (by description) | Wellington Region |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicDescription.geographicIdentifier> <MD_DataIdentification.extent> <EX_Extent> <MD_Identifier.code> |
|  | West bound of project in WGS84 co-ordinates | West longitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.westBoundLongitude> |
|  | East bound of project in WGS84 co-ordinates | East longitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.eastBoundLongitude> |
|  | South bound of project in WGS84 co-ordinates | South latitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.southBoundLatitude> |
|  | North bound of project in WGS84 co-ordinates | North latitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.northBoundLatitude> |
| Source | Contractor Contact | Metadata contact individual name | Mary Bloggs |  | <MD_Metadata.contact> <CI_ResponsibleParty.individualName> |
|  | Contractor Organisation Name | Metadata contact organisation | The Aerial Photo Company Ltd |  | <MD_Metadata.contact> <CI_ResponsibleParty.organisationName> |
|  | Contractor Contact Position | Metadata contact position | Services Manager |  | <MD_Metadata.contact> <CI_ResponsibleParty.positionName> |
|  | Contractor Role | Metadata contact role |  | Originator | <MD_Metadata.contact> <CI_ResponsibleParty.role> <CI_RoleCode> |

| Project Metadata Requirements | Description | ANZLIC (Minimum) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
| Reference Number | The source company or agency project reference number | Supplementary information |  | Contractor Reference is (number) | <gmd:identificationInfo> <gmd:MD_DataIdentification> <gmd:supplementalInformation> |
| Job Number | The contract number | Supplementary information |  | The job number is (number) | <gmd:identificationInfo> <gmd:MD_DataIdentification> <gmd:supplementalInformation> |

| Dataset Metadata Requirements | Description | ANZLIC (Core) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
|  |  | Metadata file identifier |  |  | <MD_Metadata.fileIdentifier> |
|  |  | Metadata language |  | eng | <MD_Metadata.language> |
|  |  | Metadata character set |  | Utf8 | <MD_Metadata.characterSet> |
|  |  | Metadata file parent identifier |  |  | <gmd:parentIdentifier> |
|  |  | Metadata hierarchy level |  | Dataset | <MD_Metadata.hierarchyLevel> |
|  |  | Metadata hierarchy level name |  | Dataset | <MD_Metadata.hierarchyLevelName> |
| Client (Contact Information) | Client Contact | Metadata contact individual name | Joe Bloggs |  | >MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.individualName> |
|  | Client Organisation Name | Metadata contact organisation | Land Information New Zealand |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.organisationName> |
|  | Client Contact Position | Metadata contact position | Imagery Manager |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.positionName> |
|  | Client Role | Metadata contact role |  | Owner | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_ResponsibleParty.role> <CI_RoleCode> |

| Dataset Metadata Requirements | Description | ANZLIC (Core) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
|  |  | Metadata date stamp |  |  | <MD_Metadata.dateStamp> |
| Dataset Title | Brief description of the dataset | Dataset title | 2012 Urban Specification Colour Orthophotography Wellington City |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_Citation.title> |
| Date | Date of data acquisition | Dataset reference date |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_Citation.date> <CI_Date.date> |
|  |  | Dataset reference date type |  | Creation | <MD_Metadata.identificationInfo> <MD_DataIdentification.citation> <CI_Citation.date> <CI_Date.dateType> <CI_DateTypeCode> |
| Data Description | Brief description of the dataset | Abstract |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.abstract> |
|  |  | Spatial representation type |  | Grid | </gmd:resourceConstraints> <gmd:spatialRepresentationType> <gmd:MD_SpatialRepresentationTypeCode codeList="" codeListValue="grid"/> |
|  |  | Dataset language |  | eng | <MD_Metadata.identificationInfo> <MD_DataIdentification.language> |
|  |  | Dataset character set |  | Utf8 | <MD_Metadata.identificationInfo> <MD_DataIdentification.characterSet> |
|  |  | Topic category |  | Imagery base maps earth cover | <MD_Metadata.identificationInfo> <MD_DataIdentification.topicCategory> |

| Dataset Metadata Requirements | Description | ANZLIC (Core) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
| Location | Location Description (e.g. city name, town name, region name, etc) | Geographic location of the dataset (by description) | Wellington City |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicDescription.geographicIdentifier> <MD_DataIdentification.extent> <EX_Extent> <MD_Identifier.code> |
|  | West bound of project in WGS84 co-ordinates | West longitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.westBoundLongitude> |
|  | East bound of project in WGS84 co-ordinates | East longitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.eastBoundLongitude> |
|  | South bound of project in WGS84 co-ordinates | South latitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.southBoundLatitude> |
|  | North bound of project in WGS84 co-ordinates | North latitude |  |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.extent> <EX_Extent> <EX_GeographicBoundingBox.northBoundLatitude> |
|  | Brief statement of the history of the dataset | Lineage | A new dataset. Replaces the previous dataset acquired in 2010. |  | <gmd:lineage> <gmd:LI_Lineage> <gmd:statement> |
| Source | Contractor Contact | Metadata contact individual name | Mary Bloggs |  | <MD_Metadata.contact> <CI_ResponsibleParty.individualName> |
|  | Contractor Organisation Name | Metadata contact organisation | The Aerial Photo Company Ltd |  | <MD_Metadata.contact> <CI_ResponsibleParty.organisationName> |
|  | Contractor Contact Position | Metadata contact position | Services Manager |  | <MD_Metadata.contact> <CI_ResponsibleParty.positionName> |
|  | Contractor Role | Metadata contact role |  | Originator | <MD_Metadata.contact> <CI_ResponsibleParty.role> <CI_RoleCode> |

| Dataset Metadata Requirements | Description | ANZLIC (Core) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
| Scale | Spatial resolution of the dataset | Equivalent scale | 10000 |  | <MD_Metadata.identificationInfo> <MD_DataIdentification.spatialResolution> <MD_Resolution.equivalentScale> |
| Bands | Identification of each band in the image | Image Description |  |  | <gmd:contentInfo> <gmd:MD_ImageDescription> <gmd:contentType> <gmd:MD_CoverageContentTypeCode codeList="" codeListValue="image"/> |
|  |  | Content Type |  | Image |  |
|  |  | Band Descriptor | Red | Red, Green, Blue, Alpha, etc | <gmd:dimension> <gmd:MD_Band> <gmd:descriptor> <gco:CharacterString/> |
| Projection and Datum | Projection and Datum | Reference System |  | EPSG:2193 | <MD_Metadata.referenceSystemInfo> <MD_ReferenceSystem.referenceSystemIdentifier> <RS_Identifier> |
| Medium of Ortho Photo | The medium in which the image is presented | Identification info Presentation Form |  | imageDigital | <gmd:presentationForm> |
| Ortho Image Type | File format and image type | Distribution Format | geotiff RGB |  | <gmd:distributionInfo> <gmd:MD_Distribution> <gmd:distributionFormat> <gmd:MD_Format> <gmd:name> <gmd:version> |
| Image Size | The tile dimensions of the dataset | Number of Dimensions |  | 2 | <gmd:spatialRepresentationInfo> <gmd:MD_GridSpatialRepresentation> <gmd:numberOfDimensions> |
|  |  | Dimension Name | Column | Column, or Row | <gmd:axisDimensionProperties> <gmd:MD_Dimension> <gmd:dimensionName> |
|  |  | Dimension Size | 4800 |  | <gmd:dimensionSize> |
|  |  | Units of Measure |  | pixel | </gmd:resolution> |

| Dataset Metadata Requirements | Description | ANZLIC (Core) Element | Example Entry | Default Value | Relevant ANZLIC xml tags |
| --- | --- | --- | --- | --- | --- |
| Horizontal accuracy | Horizontal tolerances of the orthophoto’s accuracy | Name of Measure |  | Horizontal accuracy | <gmd:dataQualityInfo> <gmd:report> <gmd:DQ_QuantitativeAttributeAccuracy> <gmd:nameOfMeasure> </gmd:measureDescription> |
|  |  | Measure Description | +/- 2.5 pixels |  |  |
| Sensor information | Type of camera acquiring the imagery | Supplementary Information | Original Images captured on a Leica model xxx camera with xxx focal length lens. | Original Images captured on a (camera type) camera with (any extra details required) | <MD_Metadata.identificationInfo> <gmd:supplementalInformation> |
| Pixel size | The size of each pixel in the image | Units of Measure |  | m | <gmd:spatialResolution> <gmd:MD_Resolution> <gmd:distance> <gco:Distance uom="m"></gco:Distance> |
|  |  | Distance | 0.125 |  |  |
| Positional accuracy | Horizontal tolerances of the orthophoto's accuracy | Name of Measure |  | Positional accuracy | <gmd:dataQualityInfo> <gmd:report> <gmd:DQ_QuantitativeAttributeAccuracy> <gmd:nameOfMeasure> </gmd:measureDescription> |
|  |  | Measure Description | +/- 2.5 pixel |  |  |
| Altitude | The mean height at which the original images were flown | Supplementary Information | Original images captured at a mean altitude of 1500 m. | Original images captured at a mean altitude of xxxx m. | <MD_Metadata.identificationInfo> <gmd:supplementalInformation> |

# Specifications for quality assurance of orthophotography

## Quality assessment

| Quality process | The aesthetic quality of orthophotography products will be maintained using the following process: quality plan developed by contractor and agreed to by purchaser, sample dataset provided to purchaser for review and approval, orthophotography production undertaken, and purchaser review of final orthophotography. |
| --- | --- |

| Quality plan | The contractor will develop a quality plan to achieve the aesthetic standards described in Aesthestic quality criteria, before photography commences. The quality plan will be provided to the purchaser for review. The purchaser will have agreed to the quality plan before photography commences. |
| --- | --- |

| Sample images | A set of low resolution sample raw images will be provided to the purchaser for review within six weeks of imagery acquisition. The sample will cover an area sufficient to enable the assessment of the acquisition requirements specified in section 5 of this document. This area will be agreed at the commencement of the contract. Final production of orthophotography by the contractor will not commence until the sample raw imagery has been reviewed and approved by the purchaser. A clear time period should be agreed for all reviews that require purchaser approval |
| --- | --- |

| Review of ortho-photography | The purchaser will be given the opportunity to review and approve supplied orthophotography for compliance with this specification and the quality plan prior to acceptance. Issue resolution – ongoing dialogue Most issues with the subjective aspects of orthophotography can be resolved by maintaining an open dialogue between the purchaser and contractor throughout the course of the project. A clear time period should be agreed for all reviews that require purchaser approval. |
| --- | --- |

## Aesthetic quality guidelines

| Criteria | The criteria set out in this section will be addressed in the aesthetic quality plan. |
| --- | --- |

| Radiometry | Objective To minimise inconsistent radiometry between mosaicked imagery Not Desirable through oversight, there are no radiometric corrections, sharp contrast is visible at photograph seams within a mosaic tile or between adjacent mosaic tiles, or there are significant radiometry differences among photographs. Desirable Image seams are blended to achieve, at least, a smooth seam, only minor radiometry differences exist between photographs, and radiometry is consistent among photographs without a 'checker board' appearance. |
| --- | --- |

| Brightness | Objective To ensure that all ground features can be interpreted to an agreed standard. Not Desirable ground features are not able to be interpreted in bright areas, or the imagery’s overall brightness does not meet specifications set before production. Desirable all features in bright areas are able to be interpreted, and the imagery’s overall brightness meets specifications set before production. |
| --- | --- |

| Shadows | Objective To ensure that shadowed areas contain enough detail to enable ground features interpretation. Not Desirable ground features are not interpretable in areas of shadow. Desirable ground features in shadow areas are interpretable. |
| --- | --- |

| Contrast | Objective To maintain an acceptable balance between: conserving detail in both bright and shadowed areas, and producing photographs with high contrast. Not Desirable imagery contrast is too low, or insufficient detail is discernable across a photograph. Desirable ground features can be identified across bright and shadowed areas of a photograph while maintaining high contrast. |
| --- | --- |

| Colour balance | Objective To ensure that orthophotography is provided in ‘natural colour’. Not Desirable overall imagery colour balance is not natural or is biased by a particular hue. Desirable overall imagery exhibits a ‘natural colour’ balance. |
| --- | --- |

| Foreign artefacts | Objective To minimise the number of foreign artefacts visible in photographs that obscure ground detail or features. Not Desirable more than five artefacts are present per 2.4 x 3.6 km tile, or a ground feature is obscured by a foreign artefact. Desirable less than five artefacts are present per 2.4 x 3.6 km tile, and no ground feature is obscured by a foreign artefact. |
| --- | --- |

| Elevated features | Objective To minimise the displacement of elevated features, such as buildings, which cause a leaning effect away from the photograph’s centre. Not Desirable elevated features have not been adequately corrected for leaning effects. Desirable elevated features appear vertical. |
| --- | --- |

# Text boxes

Specifications relating to the acquisition of orthophotography

In support of the National Imagery Coordination effort

July 2013

www.linz.govt.nz