| Business and Regulatory Assurance Table of Audit Items (Version 1.1 – February 2012) Pursuant to Rules for Cadastral Survey 2010 |
| --- |
| NOTE: Items sufficiently checked by the Landonline Automatic Business Rules are not included in the Table of Audit Items. |
|  | Impact assigned to Non-compliance | Rating |
|  | C S M NA | Critical Error Significant Error Minor Error Not Applicable | NA ( ( NT | Not Applicable Satisfactory Standard Unsatisfactory Standard Not Tested |

| Item | Impact | Audit Item | Rating | Comments |
| --- | --- | --- | --- | --- |
| 1.0 DATUMS |
| 1.1 Horizontal datum – orientation |
| 1.1.1 |  | Are all the new bearings in terms of the stated projection (within accuracy standards)? [Rule 4.1; Rulings LINZR65300 & 65304] |  |  |
| 1.1.2 |  | Are all the adopted bearings in terms of the stated projection (within accuracy standards)? [Rule 4.1; Rulings LINZR65300 & 65304] |  |  |
| 1.2 Horizontal datum – connection |
| 1.2.1 |  | Is the survey connected to an existing cadastral survey network mark that is located within the applicable distance specified? [Rule 4.2; LINZR65302] |  |  |
| 1.3 Vertical datum |
| 1.3.1 |  | Are reduced levels in terms of an official vertical datum when a vertical control mark is within the applicable distance specified or an alternative or an assumed datum when there are no vertical control marks within the applicable distance specified? [Rule 4.3; Rulings LINZR65301 & 65303] |  |  |
| 2.0 SURVEY DEFINITION |
| 2.1 HORIZONTAL BOUNDARIES |
| 2.1.1 |  | Is the class of survey appropriate? [Rule 3.2] |  |  |
| 2.1.2 |  | Have all of the existing parcels being extinguished been accounted for by the new parcels? [Rule 5.1] |  |  |
| 2.1.3 |  | Is the definition/ relocation of existing boundaries and boundary points correct taking into account all relevant evidence (within accuracy standards)? [Rules 6.1 & 3; Rulings LINZR65306 & 65312] |  |  |
| 2.1.4 |  | Have boundaries and boundary points been defined by survey or defined by adoption where required by the rules? [Rule 6.2] |  |  |
| 2.1.5 |  | Is the status of all old marks correct, i.e., reliable/ disturbed? [Rule 8.2] |  |  |
| 2.1.6 |  | Has a bearing adjustment been applied to adopted work where appropriate? [Rules 4.1 & 3] |  |  |
| 2.1.7 |  | Is there sufficient information within the CSD to enable all boundaries to be relocated with confidence? [Rules 8.1 & 8.2] |  |  |
| 2.2 IRREGULAR BOUNDARIES |
| 2.2.1 |  | Is the irregular boundary permitted? [Rule 6.6] |  |  |
| 2.2.2 |  | Has the position of the irregular boundary been determined to a sufficient level of accuracy? [Rule 3.4] |  |  |
| 2.3 WATER BOUNDARIES |
| 2.3.1 |  | Does the CSD correctly address the legal issues associated with the water boundary appropriately? [Rules 6.1, 6.7, 9.6.7] |  |  |
| 2.3.2 |  | Has the position of the water boundary been determined to a sufficient level of accuracy? [Rule 3.4] |  |  |
| 2.4 STRATUM BOUNDARIES |
| 2.4.1 |  | Is the definition of the stratum boundary correct (within survey tolerances)? [Rule 3] |  |  |
| 2.4.2 |  | Is there sufficient information within the CSD to enable the relationship between any position on the stratum boundary surface and any other boundary to be ascertained in accordance with the accuracy standards specified? [Rules 3.3, 3.6, 8.2 & 9.6.10] |  |  |
| 2.5 PERMANENT STRUCTURE BOUNDARIES |
| 2.5.1 |  | Does the permanent structure boundary comply with the use and type requirements specified? [Rule 6.9] |  |  |
| 2.5.2 |  | Is the definition of permanent structure boundaries correct (within accuracy standards)? [Rule 3] |  |  |
| 2.6 LIMITED TITLE, HAWKE’S BAY INTERIM TITLE, ADVERSE POSSESSION, DEEDS, BONA VACANTIA, CLAIMS |
| 2.6.1 |  | Is the position, type and age of occupation shown correctly in relation to each boundary? [Rule 9.5] |  |  |
| 2.6.2 |  | Have the boundaries been correctly defined in accordance with accepted principles? [Common Law principles, Land Transfer Act] |  |  |
| 3.0 GROUND MARKING |
| 3.1 ACCURACY OF NON-BOUNDARY AND BOUNDARY MARKS |
| 3.1.1 |  | Are non-boundary and boundary marks placed or tied to by the survey within required accuracy tolerances? [Rule 3] |  |  |
| 3.2 PERMANENT MARKS |
| 3.2.1 |  | Do all permanent reference marks satisfy mark type, location and permanence requirements? [Rule 7.4.3] |  |  |
| 3.2.2 |  | Is there a description of the permanent reference mark and its location in the CSD? [Rule 9.1] |  |  |
| 3.2.3 |  | In the case of stratum boundaries, do two permanent reference marks have reduced levels? [Rule 7.4.3] |  |  |
| 3.3 WITNESS MARKS |
| 3.3.1 |  | Do all witness marks satisfy the mark type, location and permanence requirements? [Rule 7.3.3] |  |  |
| 3.3.2 |  | In the case of stratum boundaries, is there at least one witness mark with a reduced level? [Rule 7.3.4] |  |  |
| 3.4 BOUNDARY MARKS |
| 3.4.1 |  | Are all boundary angles and intersections marked when required? [Rule 7.1] |  |  |
| 3.4.2 |  | Do all boundary marks meet requirements for type, placement and visibility? [Rule 7.2] |  |  |
| 3.5 WATER BOUNDARIES |
| 3.5.1 |  | Are water boundaries adequately described (i.e. MHWM, MHWS, tidal, top of bank etc)? [Rules 9.4 & 9.6.7] |  |  |
| 3.5.2 |  | Where the margin of the water body defining a water boundary has moved, has the water boundary been dealt with appropriately? [Rule 6.7] |  |  |
| 4.0 OCCUPATION/ PHYSICAL FEATURE |
| 4.0.1 |  | Is the nature, age and position of occupation/ physical feature correctly described and shown in relation to relevant boundaries when required? [Rule 9.5] |  |  |
| 5.0 Documentation |
| 5.1 CSD PLAN |
| 5.1.1 |  | Is the type of CSD appropriate for the survey purpose e.g. Boundary Reinstatement CSD, Monumentation CSD or other CSD type? [Rules 2 and 11] |  |  |
| 5.1.2 |  | Is the information in the CSD consistent with the field record? [Rule 14] |  |  |
| 5.1.3 |  | Does the Diagram of Survey show sufficient vectors to enable all required boundaries and points to be ascertained in accordance with the accuracy standards required? [Rules 9.6.13 & 3] |  |  |
| 5.1.4 |  | Is the Diagram of Survey clear & unambiguous and legible (at A3 for Diagram of Survey) [Rule 9.6.15] |  |  |
| 5.1.5 |  | Allowing for conversion of units of measure or the application of a bearing adjustment, has all adopted information been copied without change? [Rule 8.4] |  |  |
| 5.1.6 |  | Does the Diagram of Survey clearly depict appropriate parcel & boundary annotations and boundary dimensions? [Rules 9.6.11, 9.6.12 & 9.6.14] |  |  |
| 5.1.7 |  | Does the Diagram of Survey sufficiently depict and describe the relationship between each permanent structure boundary and other relevant boundaries? [Rule 9.6.9] |  |  |
| 5.1.8 |  | Does the Diagram of Survey contain sufficient information to enable the relationship between any position on a stratum boundary surface and all other relevant boundaries to be ascertained in accordance with accuracy standards specified? [Rules 9.6.10 & 3] |  |  |
| 5.1.9 |  | Does the Diagram of Survey adequately depict the extent of parcels and the spatial relationships between relative boundaries, including unit and cross lease area boundaries? [Rules 9.6.3, 9.6.4 & 9.6.5] |  |  |
| 5.1.10 |  | Does the Diagram of Survey correctly describe a water boundary and sufficiently depict water and irregular boundaries at a scale that clearly shows its shape and relationship to other relevant boundaries and is adequate to meet the accuracy required? [Rules 9.6.7, 9.6.8 & 3] |  |  |
| 5.2 TITLE PLAN |
| 5.2.1 |  | Is the Diagram of Parcels clear & unambiguous and legible (A4 for Diagram of Parcels)? [Rule 10.4.10] |  |  |
| 5.2.2 |  | Have parcel areas been correctly calculated from relevant boundary information? [Rule 5.3] |  |  |
| 5.2.3 |  | Does Diagram of Parcels clearly depict appropriate parcel & boundary annotations and boundary dimensions? [Rules 10.4.8 & 10.4.9] |  |  |
| 5.2.4 |  | Does Diagram of Parcels sufficiently depict and describe the relationship between each permanent structure boundary and other relevant boundaries? [Rule 10.4.7] |  |  |
| 5.2.5 |  | Does the Diagram of Parcels correctly describe a water boundary and sufficiently depict water and irregular boundaries at a scale that clearly shows its shape and relationship to other relevant boundaries? [Rules 10.4.5 & 10.4.6] |  |  |
| 5.2.6 |  | Does the Diagram of Parcels adequately depict the extent of parcels and the spatial relationships between relative boundaries, including unit and cross lease area boundaries? [Rules 10.4.2 & 10.4.3] |  |  |
| 5.2.7 |  | Are new/ existing easement and covenant details correct? [Rules 10.2 & 10.3] |  |  |
| 5.3 Reporting |
| 5.3.1 |  | Does the survey report detail all necessary information? [Rule 8.2] |  |  |